## Slide 1
H4800 Webinar
(855) 488 7655
miragescreensystems.com
T
W

## Slide 2
Today’s agenda
01.
02.
03.
04.
Introducing the Product
Going through the order form
Cost / Pricing Guideline
Installing the Product
Tips and Tricks

## Slide 3
Product Basics

## Slide 4: The H4800 Order Form - Colors

## Slide 5: H4800 Colors
Textured Black
Bronze
Champagne
Textured White
White
Tan
Textured Grey

## Slide 6: The H4800 Order Form - Sizing

## Slide 7: H4800 Sizing
Maximum Width = 22 feet (deflection beyond 16 feet, consider using cradle and large metal end caps)
Somfy motors:
  Maestra – up to 16 feet
  Altus – 16 to 22 feet
Motor placement – to closest power source. (determine by facing the front of the housing)
Power – Plug in or hard wire (plug supplied).
Electrical – 110Volts, draw of max. 3amps.
1” or 2” pile – 2” used if unlevel bottom surface.

## Slide 8: H4800 Order Form – Mounting Types

## Slide 9
Surface
In-Jamb – need L/angle brackets
Recessed – need u-channel
Make your own allowances - we build what you order.
H4800 Mounting Types

## Slide 10
H4800 Mounting Types

## Slide 11: H4800 Order Form – Remotes

## Slide 12
H4800 Remotes
1,5,16 – channel
Decoflex by
Tahoma by

## Slide 13
H4800 Remotes - Basics

## Slide 14
H4800 Fabrics

## Slide 15
H4800 Order Form - Fabrics

## Slide 16
H4800 Fabrics
Insect
Solar (about $50 more per unit than insect)
Privacy
Vinyl
Blackout
*We can source any fabric, ask your TSM

## Slide 17
H4800 Order Form – Motor

## Slide 18
H4800 - Power Cords
Antenna is in the first two feet of the cord
The cord is white, plug is black
10’ to 24’ lengths available

## Slide 19
Installation

## Slide 20: Tools of the Trade

## Slide 21: H4800 – Pre – install Photos
Overall shot:
Corner shot low:
Corner shot high

## Slide 22: H4800 – Order of Standard Install
Step 1: Mount back of cassette
Step 2: Drop in roller tube
Step 3: Center & attach screen to roller tube
Detailed install instructions are found in H4800 Module 2 on the Mirage web store.

## Slide 23: H4800 – Order of Standard Install
Step 4: Test fit front of cassette
Step 5: Mount side tracks
Step 6: Set remote limits

## Slide 24
Tips and Tricks
A level cassette is key – future problems occur otherwise
Plan/know power source location before ordering – manage customer expectations
Piece of mesh to correct unbalanced weight bar (this is called shimming)
Center mounting under header – hood access a consideration
Pigtail the cord
Antenna
Cord color
Single power for each unit – for programming
Be aware of weight bar clearance – width and height
Order L-brackets to rounded up foot
Open your box before you go to site
Bring two ladders – adequate height
Cut side tracks from bottom end

## Slide 25: Questions??